## Slide 1
National Yang Ming Chiao Tung University
SAC Path Following
for a 4-Wheel Steering Farm Robot
Progress Report · King
Notes: SAY: Today I will show three things. First, why the simulation failed before and how I fixed it. Second, the final simulation results. Third, the first test on the real robot.

## Slide 2
Three things in this presentation
1
What was wrong before
Two errors found in the model
2
What works now
Simulation results after the fix
3
What happened on the robot
First field trial and next steps
Notes: SAY: I will keep it in this order, so the reason behind the improvement is clear.

## Slide 3
Last time, I thought it was a tuning problem
It was not. The model itself was wrong.
What I believed
The reward weights were badly chosen, so I kept adjusting numbers.
10 reward versions tried.
None solved it.
What was actually true
Two errors in the robot model made the task impossible to learn.
After fixing them,
the agent learned in one run.
Notes: SAY: Last time I reported that I was tuning the reward function. That was the wrong direction. The real problem was in the robot model, not in the reward.

## Slide 4
Error 1: the robot steered the wrong way
One missing sign in the motion equation
omega = v / r_c
turn radius is always positive → direction lost
omega = sign(b) * v / r_c
direction restored → robot turns as commanded
Measured turn rate divided by the formula gave −0.961 : right size, wrong direction.
Notes: SAY: The robot turned opposite to the command, so every correction made the error bigger. I found it by comparing the measured turn rate with the formula: the ratio was minus 0.96 — correct size, wrong sign.

## Slide 5
Error 2: the real robot is much larger than modelled
Correct values came from the robot control code
 | I assumed | Reality
Wheelbase | 0.65 m | 1.72 m
Track width | 0.50 m | 1.65 m
Minimum turn radius | 0.585 m | 2.245 m
The robot cannot turn as tightly as I assumed. All earlier results were invalid, so every stage was retrained from the start.
Notes: SAY: The model used a robot 2.6 times smaller than the real one. So the simulation was solving the wrong problem. I took the true values from the robot control code and retrained everything.

## Slide 6
What each part of the controller does
Requested after the last review
Block | What it does
Kinematics | Computes how the robot body moves from the steering angles
Observation | Builds what the agent sees: deviation, heading error, path ahead
Reward | Scores progress, heading alignment and deviation at each step
Termination | Ends the run: goal reached, off track, or lost
Curriculum | Builds the path for each stage; training and testing use the same data
Notes: SAY: Each block has one job. The kinematics moves the robot, the observation describes the situation, the reward judges it, the termination stops the run, and the curriculum defines the path.

## Slide 7
Every number has a reason
No value was chosen by trial and error
Value | Where it comes from
Max steering 20.96° | Geometry: the inner wheel reaches its 31.2° limit first
Min turn radius 2.245 m | Geometry: computed from wheelbase and track width
Off-track limit 0.5 m | 5 × the 0.10 m accuracy needed between crop rows
Deviation weight 6 | Sensitivity test: 1 → 3 → 6 → 7, no further gain after 6
Minimum speed 0.2 m/s | Prevents the agent from choosing to stand still
Notes: SAY: Two values come from geometry, one from the farming accuracy requirement, one from a sensitivity test, and one prevents a degenerate solution.

## Slide 8
The agent now follows the path accurately
[ paste trajectory + CTE plot ]
0.066 m
deviation on a straight path
0.29 m
deviation on the sharpest turn
0.23 m
unavoidable by any controller
The sharpest turn is tighter than the robot can physically follow, so the agent is only 0.06 m above the geometric limit.
Notes: SAY: On a straight path the deviation is under 7 centimetres. On the sharpest turn it is 29 centimetres, but 23 of those centimetres are impossible to avoid — the turn is tighter than the robot can make.

## Slide 9
First field trial: the robot moved, but not smoothly
Worked
Control program ran on the robot
CAN link established
Robot drove and steered on command
Emergency stop worked
Problem
The robot moves in a start–stop pattern
Happens at every speed, both directions
A video exists of this robot moving smoothly, but that program was not kept
Cut short
Rain stopped the trial early
Steering calibration not done
Position sensing not done
Notes: SAY: The software side worked. The robot itself moves in a start-stop pattern, which is a hardware-side problem, not a control problem. Rain ended the session before I could finish the measurements.

## Slide 10
Next session: three things to test
One cause at a time, in this order
1
Send commands more often
Now 20 per second. Try 50, 100, 200.
2
Keep the heartbeat byte fixed
The motor controller may use it as a safety check.
3
Count failed transmissions
The original program hid them.
Goal for the next session: the robot follows the L-shaped path on its own in the field.
Notes: SAY: If none of the three explains it, the cause is outside my control program, and I will check the motor controller and the steering mechanics. The goal for next session is autonomous driving in the field.